## Slide 1
Professional English for Geographical Information System

## Slide 2
Part Ⅰ The Basic Concept of GIS
1. What is GIS? (L.1)
2. What kinds of functions does a GIS have? (L.2)

## Slide 3
Part Ⅰ ——1. What is GIS?
Geographic (/,dʒi:ə'ɡræfik/) information system——United States
Geographical (/,dʒi:ə'ɡræfikl/) information system——European
Geomatique (地理信息技术) ——Canada

## Slide 4
People
Hardware
Software
Data
Methods
GIS
Figure Components of GIS

## Slide 5
Part Ⅰ ——1. What is GIS?
The GIS has four subsystems:
1）A data input subsystem that collects and preprocesses spatial data from various sources.
2）A data storage and retrieval (/ri’tri:vəl/) subsystem that organizes the spatial data in a manner that allows retrieval, updating, and editing.

## Slide 6
Part Ⅰ ——1. What is GIS?
The GIS has four subsystems:
1）A data input subsystem
2）A data storage and retrieval subsystem
3）A data manipulation (/mə,nipju’leʃən/) and analysis subsystem that performs tasks on the data, aggregates(合并/’æɡriɡit/) and disaggregates, estimates parameters and constraints (约束条件/kən’streint/), and performs modeling functions (函数).
4）A reporting subsystem that displays all or part of the database in tabular, graphic, or map form.

## Slide 7
Part Ⅰ——2. What kinds of functions does a GIS have?
1）Data input subsystem
Input: “encoded” (points, lines, areas) into the computer from a collected source.
Sources:
Aerial (/’ɛriəl/) photography ——航空照片，航空摄影
Digital remote sensing ——数字遥感
Surveying ——测量
Digital line graph (/ɡræf/)(DLG) ——数字线划地图(矢量)
Digital elevation (/٫elə’veiʃən/) models (DEM) ——数字高程模型
Digital orthophoto /‘ɔ:θəu/ map(DOM) ——数字正射影像
Visual descriptions ——视觉描述(可视化)
Statistical data ——统计数据

## Slide 8
Part Ⅰ——2. What kinds of functions does a GIS have?
2）Data storage and retrieval subsystem
Points, lines, areas are stored as grid cells or coordinate (/kəu'ɔ:dineit/) pairs and pointers in computer.
Attribute tables are associated with coordinate pairs.
Retrieval requires efficient computer search techniques.

## Slide 9
Part Ⅰ——2. What kinds of functions does a GIS have?
3）Data manipulation and analysis subsystem
——the heart of the GIS
Uses the power of the computer to measure, compare, and describe contents of the database.
Allows ready access to the raw data and allows aggregation and reclassification for further analysis.

## Slide 10
Part Ⅰ——2. What kinds of functions does a GIS have?
4）Reporting and output subsystem
The map is only one type of GIS output.
Also includes tables, charts(图表), diagrams (曲线图), photographs (照片).

## Slide 11
Datasource
Real World
Spatial Database
User
GIS system
Capturing
Spatial data
Spatial data
Input
Spatial data
Management
Decision
Support
Solve Spatially Referenced Problems

## Slide 12
Part Ⅰ——2. What kinds of functions does a GIS have?
Land information system
Parcel-based LIS
CAD/CAM

## Slide 13
Part Ⅱ Data Structure
and Database of GIS
1. GIS data models (L. 6)
2. Digital elevation modeling (L. 14)

## Slide 14
Part Ⅱ——1. GIS data models
GIS stores information about the world as a collection of thematic layers(专题图层) that can be linked together by geography.
This approach allows us to organize the complexity of the world into a simple representation to help facilitate (/fə’siliteit/) our understanding of nature relationships.

## Slide 15
Part Ⅱ——1. GIS data models
1）GIS data types
The basic data types in a GIS reflects traditional data found in a map.
Spatial data: describes the absolute (/’æbsəlu:t/) and relative location of geographic features(地理要素).
Attribute data: describes characteristics of the spatial features(空间要素).

## Slide 16
Part Ⅱ——1. GIS data models
2）Spatial data models
Vector (矢量)
Raster (栅格)
Image(影像)：Reflects pictures or photographs of the landscape, very similar to raster data, however typically lacks the internal formats(格式) required for analysis and modeling(建模) of the data.

## Slide 17
Part Ⅱ——1. GIS data models
3）Vector data formats
Vector storage implies the use of vectors (directional lines) to represent a geographic feature.
Coverage (数据层, /’kʌvəridʒ/)——Spatial relationship model, topology(拓扑, /tə’pɔlədʒi/)--Arcinfo
Shapefile (数据层)——Spatial relationship model, non topology(非拓扑)--Arcview
Geodatabase (空间数据库或地理数据库)——Object-based model--ArcGIS

## Slide 18
Part Ⅱ——1. GIS data models
3）Vector data formats（map structure）
Annotation (注记, /,ænəu'teiʃən/): text labeling
Arcs (弧段) : line segments (线段) forming polygon borders (边界) or individual linear features (线性要素)
Polygons (多边形, /’pɔli:,gɔn/): areas enclosed(闭合) by arcs
Points (点) : single coordinate pairs.
Nodes (节点) : points at the end of arcs
Vertices (vertex) (顶点) : points along an arc
Discrete points (离散点) : individual point features, polygon centers or text positions
Tics (控制点) : registration(配准/٫redʒi’streiʃən/ ) control points

## Slide 19
Part Ⅱ——1. GIS data models
4）Raster data formats（map structure）
Raster data models incorporate(吸收) the use of a grid-cell data structure where the geographic area is divided into cells identified by row (行) and column (列).
Coverage (数据层): set of map features
Annotation (注记): text labeling
Surface (表面): continuous gradient (梯度)

## Slide 20
Part Ⅱ——1. GIS data models
4）Raster data formats（map structure）
Area (地区): set of partial and whole cells forming areal (面状) features.
Lines (线): set of partial cells forming borders or linear features.
Cells (单元格): single column, row position.
Partial(部分): locations with attributes in just part of a cell.
Whole (全部): locations with attributes throughout the entire cell.
Tics (控制点) : registration(配准) control points.

## Slide 21
Part Ⅱ——1. GIS data models
5）Image data
Image data is typically used in GIS as background display data or as a graphic (图形) attribute.
Remote sensing software makes use of image data for image classification (分类) and processing (处理).
Typically, the image data must be converted (转换) into a raster format (and perhaps vector) to be used analytically (/,ænə’litikli ) with the GIS.

## Slide 22
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Vector data advantages:
①Data can be represented at its original resolution (分辨率, /,rezə’lu:ʃən/) and form without generalization (归纳，综合，综合处理).
②Graphic (图形) output is usually more aesthetically (审美地, /i:s'θetikəli/) pleasing.
③ Since most data is in vector form, no data conversion is required.

## Slide 23
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Vector data advantages:
④Accurate/’ækjərət/ geographic location of data is maintained.
⑤Allows for efficient encoding of topology (拓扑编码), and as a result, more efficient operations (运算) that require topological information are possible, e.g. proximity (邻域, /prɔk'simiti/), network (网络) analysis.

## Slide 24
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Vector data disadvantages:
①The location of each vertex needs to be stored explicitly (明确地).
②For effective analysis, vector data must be converted into a topological structure (拓扑结构). This usually requires extensive data cleaning (数据整理). As well, topology is static (静态的), and any updating or editing of the vector data requires re-building of the topology (拓扑重建).

## Slide 25
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Vector data disadvantages:
③Algorithms (算法, /‘ælɡə,riðəm/) for manipulative (操纵,处理) and analysis functions are complex and may be processing intensive. Often, this inherently limits the functionality for large data sets.

## Slide 26
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Vector data disadvantages:
④Continuous data, such as elevation (高程) data, is not effectively represented in vector form. Usually substantial (大量, / səb'stænʃəl/) data generalization or interpolation (插值, /in,təpəu'leiʃən/) is required for these data layers.
⑤Spatial analysis and filtering (过滤，处理) within polygons is impossible.

## Slide 27
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Raster data advantages:
①The geographic location of each cell is implied by its position in the cell matrix (单元格矩阵). Accordingly, other than an origin point (原点,通常左下角), no geographic coordinates are stored.
②Due to the nature of the data technique, data analysis is usually easy to program (编程) and quick to perform (运行).
③The inherent /in’hiərənt/ nature of raster maps, e. g. one attribute maps, is ideally suited for mathematical modeling and quantitative analysis.

## Slide 28
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Raster data advantages:
④Discrete data (离散数据), e. g. forestry stands, is accommodated (适于) equally(to raster data) well as continuous data, e. g. elevation data, and facilitates the integrating (集成，整合) of the two data types.
⑤Grid-cell systems (网格系统) are very compatible (兼容的, /kəm'pætəbl/ ) with raster-based output devices, e. g. electrostatic plotters (电子绘图仪), graphic terminals (图形终端).

## Slide 29
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Raster data disadvantages:
①The cell size determines the resolution at which the data is represented.
②It is especially difficult to adequately represent linear features depending on the cell resolution. Accordingly, network linkages (网络连接) are difficult to establish.
③Processing of associated attribute data (关联属性数据) may be cumbersome (麻烦的, /'kʌmbəsəm/ ) if large amounts of data exists. Raster maps inherently reflect only one attribute or characteristic for an area.

## Slide 30
Part Ⅱ——1. GIS data models
6）Vector and raster—advantages and disadvantages
Raster data disadvantages:
④Since most input data is in vector form, data must undergo vector-to-raster conversion (矢量-栅格转化). Besides increased processing requirements this may introduce data integrity concerns (担忧，顾虑) due to generalization and choice of inappropriate cell size.
⑤Most output maps from grid-cell systems do not conform to high-quality cartographic (制图的/,kɑ:tə'ɡræfik/) needs.

## Slide 31
Part Ⅱ——2. Digital elevation modelling
Digital elevation model (DEM): a digital representation of ground surface topography (地貌, /tə'pɔgrəfi:/) or terrain(地形, /te'rein/)
Digital terrain model (DTM) ): 数字地形模型

## Slide 32
Part Ⅱ——2. Digital elevation modelling
DEM form an integral(必须的, /'intiɡrəl/) part of GIS and most often used for:
①Hydrological (水文, /hai'drɔlədʒikl/ ) models including flood simulation (洪水模拟), delineation (界定, /di,lini'eiʃn/ ) and analysis of watersheds (流域) and drainage /’dreinidʒ/ networks (排水网络).
②Soil erosion (土壤侵蚀) and sediment(沉积物) transport modeling.
③ Delineation and study of physiographic units (地文单元/ 'fizi:əu'græfik/)

## Slide 33
Part Ⅱ——2. Digital elevation modelling
DEM form an integral(必须的) part of GIS and most often used for:
④Soil and ecological studies.
⑤Geomorphological (地形学的，地貌学的/, mɔ:fə'lɔdʒikəl/) evaluation of landforms.
⑥Civil engineering (土木工程) and military applications (军事应用) such as site and route selection, landslide hazard assessment (滑坡风险评估), visibility analysis (能见度分析).
⑦Remotely sensed image enhancement for 3D analysis.

## Slide 34: P44
Systems based on quadtrees are called variable resolution systems because they can operate at any level of quadtree subdivision. If you do not need high resolution for your computations—in other words, if details is not essential—you can use a rather coarse level of resolution(or quadtree subdivision) in your analysis. Thus users can decide how fine the resolution needs to be for various manipulations. In addition, because of the compactness of storage from this method, very large databases, perhaps continental or even global scales, can be stored in a single system.

## Slide 35
Part Ⅲ Acquisition(/,ækwi'ziʃən/) of spatial data
1. Data sources (L.15)
2. Data input techniques (L.15)
3. Data editing and quality assurance (L.16)
4. Surveying (L.17)
5. Satellite positioning system (L.18)

## Slide 36
Part Ⅲ—— 1. Data sources
Base data represents information which is collected and encoded into the GIS database.
Derived data are created through algorithms, such as the derivation of slope from an elevation map.
Interpreted data involve the calibration(/,kælə'breiʃən/) and modeling of base and derived maps in the expression of a GIS application.
Base Data
Elevation
Roads
Water
Vegetation
structures
Political data
Features
Ownership
Soils
Parent rock
┅
Derived Data
Slope
aspect
Watersheds
Stream buffer
Viewsheds(视域)
Accessibility(通达性)
Covertype diversity
Housing density
┅
Interpreted Data
Habitat
Aesthetics (/ i:s'θetiks /美学)
Best route
Harvesting schedule
┅

## Slide 37
Part Ⅲ—— 2. Data input techniques
(1) Manual digitizing(/'didʒitaiz/)
(2) Automatic scanning(扫描)
(3) Coordinate geometry (/dʒi'ɔmitri/)
(4) Conversion of existing digital data

## Slide 38
Part Ⅲ——2. Data input techniques
A digitizer(数字化仪) is an electronic device consisting of a table upon which the map or drawing is placed.
The user traces (跟踪) the spatial features with a hand-held magnetic (磁性, /mæɡ'netik/) pen, often called a mouse or cursor. While tracing the features the coordinates of selected points are sent to the computer and stored.
(1) Manual digitizing

## Slide 39
Part Ⅲ——2. Data input techniques
All points that are recorded are registered against positional control points (控制点), usually the map corners, that are keyed in by the user at the beginning of the digitizing session.
The building of topology (建立拓扑关系) is primarily a post-digitizing process that is commonly executed in batch mode(批量处理/bætʃ/) after data has been cleaned.
(1) Manual digitizing

## Slide 40
Part Ⅲ——2. Data input techniques
Manual digitizing has many advantages:
① Low capital cost, e. g. digitizing tables are cheap.
②Flexibility and adaptability (适应性/ə,dæptə'biləti/) to different data types and sources.
③Easily taught in a short amount of time--an easily mastered skill.
④Generally the quality of data is high.
⑤Digitizing devices are very reliable and most often offer a greater precision that the data warrants (保证/'wɔrənt/).
⑥Easily register (记录) and update (更新) existing data.
(1) Manual digitizing

## Slide 41: Precision farming yields many gains
The Chinese government's No 1 central document released in February attached great importance to high-tech agriculture.
Everyone thinks high-tech farming means biotechnology, but it actually goes far beyond that. Biotech seeds are now being upstaged in the United States by a variety of "precision farming" technologies, such as drip irrigation and GPS guidance systems, that offer savings in the use of water and chemical inputs.
On big farms in the US four out of five tractors are now equipped with GPS systems that “auto-steer(驾驶)" the equipment in perfectly straight lines. With differential correction signals, these systems can tell a machine exactly where it is in a field, down to 1 square meter. This in turn allows on-board computers to access GIS mapping data and instruct the machine to apply fertilizer or lime at differential rates, location by location. This eliminates both under-application that can hold down yields and over-application that wastes money and pollutes the environment.

## Slide 42
Part Ⅲ——2. Data input techniques
Automatic scanning has the advantage of being able to capture spatial features from a map at a rapid rate of speed.
But it has some practical limitations:
① Hard copy maps(硬拷贝地图) are often unable to be removed to where a scanning device is available, e. g. most companies or agencies (/’eidʒənsi/) cannot afford their own scanning device and therefore must send their maps to a private firm for scanning.
②Hard copy data may not be in a form that is viable (可行的/’vaiəbəl/) for effective scanning, e. g. maps are of poor quality, or are in poor condition.
(2) Automatic scanning(扫描)

## Slide 43
Part Ⅲ——2. Data input techniques
But it has some practical limitations:
③Geographic features may be too few on a single map to make it practical to scan.
④Often on busy maps a scanner may be unable to distinguish the features to be captured from the surrounding graphic information, e. g. dense contours (等高线/,kɔn’tuə/) with labels.
⑤With raster scanning it is difficult to read unique labels for a geographic feature effectively.
⑥Scanning is much more expensive than manual digitizing, considering all the cost/performance(性能) issues.
(2) Automatic scanning(扫描)

## Slide 44
Part Ⅲ——2. Data input techniques
Consensus (共识, /kən’sensəs/) within the GIS community indicates that scanners work best when the information on a map is kept very clean, very simple, and uncluttered (整齐的，不冲突的) with graphic symbols.
Currently, general consensus is that the quality of data captured from scanning methods is not substantial (值得的，相当的) enough to justify the cost of using scanning technology.
(2) Automatic scanning(扫描)

## Slide 45
Part Ⅲ——2. Data input techniques
However, major breakthroughs (突破, /,breik’θru:/) are being made in the field, with scanning techniques and with capabilities to automatically clean and prepare scanned data for topological encoding. These include a variety of line following (线跟踪) and text recognition (文本识别) techniques. Users should be aware that this technology has great potential in the years to come, particularly for larger GIS installations.
(2) Automatic scanning(扫描)

## Slide 46
Part Ⅲ——2. Data input techniques
Coordinate geometry (COGO) procedures(/prə’si:dʒə/, 过程，步骤) involves entering, from survey data, the explicit (/iks’plisit/) measurement of features from some known monument (基准点). This input technique is obviously very costly and labor intensive (加强的，集约的).
This method is more appropriate for land records management at the cadastral (地籍的/kə’dæstrəl/) or municipal (市政的/mju’nisipəl/) scale.
(3) Entry of coordinates using coordinate geometry

## Slide 47
Part Ⅲ——2. Data input techniques
This technique is becoming increasingly popular for data input.
Most GIS software vendors (供应商) also provide an ASCII (American Standard Code for Information Interchange, 美国信息交换标准代码) data exchange format specific to their product, and a programming subroutine (子程序) library that will allow users to write their own data conversion routines to fulfill their own specific needs.
As digital data becomes more readily available this capability becomes a necessity for any GIS.
(4) Conversion of existing digital data

## Slide 48
Part Ⅲ——3. Data editing and quality assurance
Data editing and verification (核实，验证) is in response to (对…做出反应) the errors that arise during the encoding of spatial and non-spatial data. The editing of spatial data is a time consuming (/kən’sju:m/ ), interactive (交互的) process that can take as long, if not longer, than the data input process itself.

## Slide 49
Part Ⅲ——3. Data editing and quality assurance
Several kinds of errors can occur (/ə’kə:/) during data input. They can be classified as:
①Incompleteness of the spatial data. This includes missing points, line segments, and/or polygons.
②Locational placement (放置) errors of spatial data. These types of errors usually are the result of careless digitizing or poor quality of the original data source.
③Distortion (失真，扭曲，/di’stɔ:ʃən/) of the spatial data. This kind of error is usually caused by base maps that are not scale-correct (比例尺) over the whole image, e. g. aerial photographs, or paper documents.

## Slide 50
Part Ⅲ——3. Data editing and quality assurance
Several kinds of errors can occur during data input. They can be classified as:
④Incorrect linkages between spatial and attribute data. This type of error is commonly the result of incorrect unique identifiers (labels) (标识符号) being assigned during manual key in or digitizing. This may involve the assigning of an entirely wrong label to a feature, or more than one label being assigning to a feature.
⑤Attribute data is wrong or incomplete. Often the attribute data does not match exactly with the spatial data. This is because they are frequently from independent sources and often different time periods. Missing data records or too many data records are the most common problems.

## Slide 51
Part Ⅲ——3. Data editing and quality assurance
The identification (/ai,dentifi’keiʃən/) of errors in spatial and attribute data is often difficult. Most spatial errors become evident during the topological building process. The use of check plots (对照区) to clearly determine where spatial errors exist is a common practice. Most topological building functions in GIS software clearly identify the geographic location of the error and indicate the nature of the problem.
Experience indicates that in the course of any GIS project 60% to 80% of the time required to complete the project is involved in the input, cleaning, linking, and verification of the data.

## Slide 52
Part Ⅲ——3. Data editing and quality assurance
(1) Spatial data errors (p98)
The most common problems that occur in converting data into a topological structure include:
Slivers (碎片) and gaps (缺口) in the line work.
Dead ends, e. g. also called dangling arcs (/'dæŋɡl/悬挂线), resulting from overshoots and undershoots in the line work.
Bow ties (蝴蝶结) or weird polygons (/wiəd/不正规多边形) from inappropriate closing of connecting features.

## Slide 53
Dangling
Sliver
weird polygons

## Slide 54
Part Ⅲ——3. Data editing and quality assurance
(1) Spatial data errors
①Slivers are the most common problem when cleaning data.
Slivers frequently occur when coincident (一致的) boundaries are digitized separately, e. g. once each for adjacent (毗邻的，/ə’dʒeisənt/) forest stands (林地), once for a lake and once for the stand boundary, or after polygon overlay (叠加).
Slivers often appear when combining data from different sources, e. g. forest inventory, soil, and hydrography (水文地理学/hai’drɔɡrəfi/; hydrology).
It is advisable to digitize data layers with respect to an existing data layer rather than attempting to match data layers later.

## Slide 55
Part Ⅲ——3. Data editing and quality assurance
(1) Spatial data errors
②Dead ends usually occur when data has been digitized in a spaghetti (绝缘/spə’geti/) mode, or without snapping (对象捕捉，捕获) to existing nodes. Most GIS software will clean up undershoots and overshoots based on a user defined tolerance (容差), e. g. distance.
③The definition of an inappropriate /,inə’prəupriət/ distance often leads to the formation of bow ties or weird polygons during topological building. Tolerances that are too large will force arcs to snap one another that should not be connected. The results is small polygons called bow ties.

## Slide 56
Part Ⅲ——3. Data editing and quality assurance
(1) Spatial data errors
④The other problem that commonly occurs when building a topologic data structure is duplicate lines (/’dju:plikit/).
These usually occur when data has been digitized or converted from a CAD system. The lack of topology in these type of drafting systems permits the inadvertent (疏忽的 /,inəd'və:tənt /) creation of elements that are exactly duplicate.

## Slide 57
Part Ⅲ——3. Data editing and quality assurance
(1) Spatial data errors
However, most GIS packages afford automatic elimination (消除, /I,limi’neiʃən/) of duplicate elements during the topological building process.
Most GIS software will provide the capability to eliminate bow ties and slivers by means of a feature elimination command based on area, e. g. polygons less than 100 square meters.
The ability to define custom topological error scenarios (方案, /si’neəri:,əu/) and provide for semi-automated correction is a desirable capability for GIS software.

## Slide 58
Part Ⅲ——3. Data editing and quality assurance
(2) Attribute data errors
The identification of attribute data errors is usually not as simple as spatial errors. This is especially true if these errors are attributed to (归因于) the quality or reliability of the data. Errors as such usually do not surface until later on in the GIS processing.
Solutions to these type of problems are much more complex and often do not exist entirely. It is much more difficult to spot errors in attribute data when the values are syntactically (在语法构成上, /sin'tæktikəli/) good, but incorrect.

## Slide 59
Part Ⅲ——3. Data editing and quality assurance
(2) Attribute data errors
Simple errors of linkage, e. g. missing or duplicate records, become evident during the linking operation between spatial and attribute data. Again, most GIS software contains functions that check for (检查) and clearly identify problems of linkage during attempted operations. This is also an area of consideration when evaluating GIS software.

## Slide 60
Part Ⅲ——3. Data editing and quality assurance
(3) Data verification
Six clear steps stand out in the data editing and verification process for spatial data:
①Visual review (目测). This is usually by check plotting(样区).
②Cleanup of lines and junctions (连接点). This process is usually done by software first and interactive editing second.
③Weeding of excess coordinates. This process involves the removal of redundant (多余的) vertices (/’vɚti,siz/) by the software for linear and/or polygonal features.

## Slide 61
Part Ⅲ——3. Data editing and quality assurance
(3) Data verification
Six clear steps stand out in the data editing and verification process for spatial data:
④Correction for distortion and warping. Most GIS software has functions for scale correction (比例尺修正) and rubber sheeting (拉伸变形). However, the distinct rubber sheet algorithm used will vary depending on the spatial data model, vector or raster. Some raster techniques may be more intensive than vector based algorithms.

## Slide 62
Part Ⅲ——3. Data editing and quality assurance
(3) Data verification
Six clear steps stand out in the data editing and verification process for spatial data:
⑤Construction of polygons. Since the majority of data used in GIS is polygonal, the construction of polygon features from lines/arcs is necessary. Usually this is done in conjunction (联合) with the topological building process.
⑥The addition of unique identifiers or labels. Often this process is manual. However, some systems do provide the capability to automatically build labels for a data layer.

## Slide 63
Part Ⅲ——3. Data editing and quality assurance
(3) Data verification
These data verification steps occur after the data input stage and prior to or during the linkage of the spatial data to the attributes. Data verification ensures the integrity (完整/in’tegrəti/) between the spatial and attribute data.
Verification should include some brief querying (查询/’kwiəri /) of attribute and cross checking (交互核对，交叉检查) against known values.

## Slide 64
Part Ⅲ——4. Surveying
Modern surveying is computerized: a total station theodolite (全站经纬仪, / θi'ɔdəlait/) can now store and process digital measurement data either in the field or, subsequently (随后, /’sʌbsikwəntli/), through an interface (接口) to a computer. Data may be coded or assigned themes in subsequent computer editing.

## Slide 65
Part Ⅲ——4. Surveying
Survey point location accuracy usually varies from ±(plus-minus) 1 to ±10 cm, depending on how measurements are made.
Surveying is usually employed whenever up-to-date (最新的) and accurate information is needed for ground control points (地面控制点) and measurement of property lines, buildings, manhole (检修孔) location, and the like, as well as for smaller areas and for other details that have to be measured accurately. Surveying of complete terrain details can cover about 0.1 to 0.2 hectares (ha, /’hektɛə/) per hour.
Photogrammetry (摄影测量) is usually employed in mapping larger areas.

## Slide 66
Part Ⅲ——4. Surveying
Survey data may be entered in GIS wherever accurate map data are required—for example, when determining property borders for legal (/’li:ɡl/) purposed. New data that are intended (准备 /in’tend/) for computers are transformed in digital form to GIS. However, larger amounts of older analog (模拟/’ænəlɔ:g/) data are available (可用的/) where coordinates have to be keyed in manually. Data for each property should be verified, by identifying nodes and closing polygons.

## Slide 67
Part Ⅲ——4. Surveying
This process is time-consuming—two or three times longer than the corresponding task using a digitizer, inclusive (包括) of all preparatory (预备的，/pri’pærə,təri/) and editing tasks. However, the data produced are easier to apply than digitizer data.

## Slide 68
Part Ⅲ——5. Satellite positioning system
The global positioning system (GPS) is a military satellite-based navigational (导航/,nævi'geiʃənəl/) system developed by the U. S. Department of Defense.

## Slide 69
Part Ⅲ——5. Satellite positioning system
Because in using the formulas(公式) we operate with differences (差值) in distance in space, it is correct to say that with GPS, vectors (矢量线段) are measured instead of distance.
Treatment of the measurement readings (读数) is thus based on calculation of the vector in a coordinate system with the Earth’s center as origin. GPS is based on the WGS84 as datum (基准) and on geocentric (地心，/,dʒiəu'sentrik/ ) coordinate system, which may be transformed to other coordinate systems.

## Slide 70
Part Ⅲ——5. Satellite positioning system
Normally, GPS yields an accuracy of approximately (/ə'prɑ ksimətli/) ±25 m with no further correction. Accuracy can be increased further by combining data from two receivers simultaneously (同时, /saiməl'teiniəsli/), provided that one receiver (the reference station) is placed at a ground control point.

## Slide 71
Part Ⅲ——5. Satellite positioning system
The difference between the given coordinates at the reference station and the calculated GPS coordinates provides a basis for correcting new GPS-measured points in the area. This is called differential GPS (差分GPS) measurement. This kind of differential measurement can determine the accuracy of new points to a few centimeters.

## Slide 72
Part Ⅲ——5. Satellite positioning system
In addition to measuring methods, accuracy is dependent on the distance between stations, measuring time, and the satellite's position in relation to the point to be determined. Normally, accuracy will be reduced by a distance of about 0.5 cm per kilometer from the reference station.

## Slide 73
Part Ⅲ——5. Satellite positioning system
Accuracy in centimeter is attainable by virtue of extensive (广泛的), rapid computations of error corrections. In the field (野外), relatively straightforward real-time differential (实时差分) measurement and computations may result in a position being determined to an accuracy of ±5 to ±10 m, as for cars and ships in motion. In some countries a service has been established that broadcasts (广播) GPS corrections over the radio and phone network. This is particularly useful in boat and vehicle navigation.

## Slide 74
Part Ⅲ——5. Satellite positioning system
One of the drawbacks(缺点) of GPS is that it requires a direct line of sight (视线) between the receiver and each satellite accessed. In many instances the terrain, buildings, trees, and other objects may block the satellites from view or may distribute (分散，干扰) the signals (信号).

## Slide 75
Part Ⅲ——5. Satellite positioning system
So, GPS is most useful for:
①Locating new survey control stations and upgrading the accuracy of old station positions.
②Determining points in property boundaries.
③Measuring terrain features that are difficult to measure by conventional (常规的, /kən'venʃənl /) means.
④Positioning offshore oil platforms.
⑤Updating road data with a GPS receiver in a car.
⑥Marine (海洋/mə'ri:n/) navigation, including integration with electronic charts.
⑦Car navigation.
⑧Determining camera-carrying aircraft positions to reduce reliance on fixed marks in aerial photography (航空摄影).
⑨Determining difference in elevation.

## Slide 76
Part Ⅲ——5. Satellite positioning system
GPS has been integrated (集成) directly with several GISs. In general, GPS data may be regarded in the same way as other digital map data. Coding of GPS data in GIS may be performed in the field to determine accurately the positions of intersections (交叉点) , road signs (路标), the ends of bridges, road surfaces, and the like.

## Slide 77
Part Ⅲ——5. Satellite positioning system
The cost of a GPS receiver depends in part on the accuracy it can achieve. High-precision receivers like those used in geodesy (大地测量学, /dʒi:'ɔdisi/) are the most expensive.
At present, they are slightly more expensive than electronic theodolites (经纬仪, /θi'ɔdəlait/). However, GPS instruments are becoming less expensive and are so efficient that they are taking over (接管) most traditional surveying areas.

## Slide 78
The best-known map projection coordinate system is the UTM Grid, established by the U. S. Department of Defence in 1947. UTM is based on a special type of cylindrical(圆柱形的/sə’lindrikl/) projection known as the Universal Transverse(横向的) Mercator(通用横轴墨卡托). UTM covers the surface of the Earth from 84 degrees North to 80 degrees South with the help of 60 zones, and each zone has a width of 6 degrees. The zones are numbered eastward from 1 to 60, starting west of continental Alaska. The central meridian(子午线/mə'ridiən/) in each zone represents the zone’s north-south axis, and the origo(起点/‘ɔ:rigəu/) of the coordinate system lies at the meeting point of axes and the equator. Thus, the equator represents the zone’s east-west axis.

## Slide 79
Part Ⅳ Spatial analysis
1. Manipulation and transformation of spatial data (L21)
2. Integration (集成) and modeling of spatial data (L21)
3. Integrated analytical (综合分析 /,ænə'litikl/) functions in a GIS (L22)

## Slide 80
Part Ⅳ——1. Manipulation and transformation of spatial data
(1) Coordinate thinning (坐标稀疏化)
(2) Geometric transformations (几何变换)
(3) Map projection transformations (地图投影变换)
(4) Conflation (合并, /kən'fleiʃən/), sliver removal (碎片删除)
(5) Edge matching (边界匹配)
(6) Interactive graphic editing (交互图形编辑)

## Slide 81
Part Ⅳ——1. Manipulation and transformation of spatial data
(1) Coordinate thinning (坐标稀疏化) : involves the weeding or reduction of coordinate pairs, e. g. X and Y, from arcs.
This function is often required when data has been captured with too vertices for the linear features. This can result in redundant (多余的/ri’dʌndənt/) data and large data volumes (数据量). The weeding of coordinates is required to reduce this redundancy (冗余度).

## Slide 82
Part Ⅳ——1. Manipulation and transformation of spatial data
(1) Coordinate thinning (坐标稀疏化) : involves the weeding or reduction of coordinate pairs, e. g. X and Y, from arcs.
This function is also required in the map generalization (地图综合) process of linear simplification (线要素化简). Linear simplification is one component of generalization that is required when data from one scale, e. g. 1:20,000, is to be used and integrated with data from another scale, e. g. 1:100,000. Coordinate thinning is often done on features such as contours (/,kɔn’tuə/), hydrography (水道), and forest stand boundaries.

## Slide 83
Part Ⅳ——1. Manipulation and transformation of spatial data
(2) Geometric transformations (几何变换)
This function is concerned with the registering (配准) of a data layer to a common coordinate scheme. This usually involves registering selected data layers to a standard data layer already registered. The term rubber sheeting (拉伸) is often used to describe this function. Rubber sheeting involves stretching one data layer to meet another based on predefined control points of known locations.

## Slide 84
Part Ⅳ——1. Manipulation and transformation of spatial data
(2) Geometric transformations (几何变换)
For example, often classified satellite imagery may require warping to fit an exiting forest inventory layer, or a poor quality vector layer may require warping to match a more accurate raster layer.

## Slide 85
Part Ⅳ——1. Manipulation and transformation of spatial data
(3) Map projection transformations (地图投影变换)
This functionality concerns the transformation of data in geographic coordinates for an existing map projection to another map projection.
Most GIS software requires that data layers must be in the same map projection for analysis. Accordingly, if data is acquired in a different projection from the other data layers it must be transformed.
Typically 20 or more different map projections are supported in a GIS software offering.

## Slide 86
Part Ⅳ——1. Manipulation and transformation of spatial data
(4) Conflation (合并, /kən'fleiʃən/), sliver removal (碎片删除)
Conflation is formally defined as the procedure of reconciling (协调, 匹配, /'rekənsail /) the positions of corresponding features in different data layers. More commonly this is referred to as (被称为) sliver removal.

## Slide 87
Part Ⅳ——1. Manipulation and transformation of spatial data
(4) Conflation (合并, /kən'fleiʃən/), sliver removal (碎片删除)
Often two layers that contain the same feature, e. g. soils and forest stands both with a specific lake, do not have exactly the same boundaries for that features. This may be caused by a lack of coordination (协调, /kəu,ɔ:dn'eiʃən/ ) or data prioritization (数据优先级, /prai'ɔriti/) during digitizing or by different manipulation and analysis techniques. When the two layers are combined, e. g. normally in polygon overlay (多边形叠加), they will not match precisely and small sliver polygon will be created. Conflation is concerned with(涉及，关注) the process for removing these slivers and reconciling the common boundary.

## Slide 88
Part Ⅳ——1. Manipulation and transformation of spatial data
(4) Conflation (合并), sliver removal (碎片删除)
There are several approaches for sliver removal:
①Perhaps the most common is allowing the user to define a priority (优先级, /prai'ɔriti/) for data layers in combination with a tolerance value (容差值). Considering the soils and forest stand example the user could define a layer that takes precedence (优先权, /'presidəns/), e. g. forest stands, and a size tolerance for slivers. After polygon overlay if a polygon is below the size tolerance it is classified a sliver. To reconcile the situation the arcs of the data layer that has higher priority will be retained and the arcs of the other data layer will be deleted.

## Slide 89
Part Ⅳ——1. Manipulation and transformation of spatial data
(4) Conflation (合并), sliver removal (碎片删除)
There are several approaches for sliver removal:
②Another approach is to simply (/‘simpli/) divide the sliver down the centre and collapse (压缩, /kə’læps/) the arcs making up the boundary. The important point is that all GIS software must have the capability to resolve slivers. Remember that it is generally much less expensive to reconcile maps (协调) manually in the map preparation and digitizing stage than afterwards.

## Slide 90
Part Ⅳ——1. Manipulation and transformation of spatial data
(5) Edge matching (边界匹配)
Edge matching is simply the procedure to adjust the position of features that extend across (跨越) typical map sheet (图幅) boundaries.
Theoretically (理论上 /,θiə‘retikli/) data from adjacent (/ə’dʒeisnt/) map sheets should meet precisely at map edges. However, in practice this rarely occurs. Misalignment (错位，偏差 /,misə'lainmənt/) of features can be caused by several factors including digitizing error, paper shrinkage (皱缩, /'ʃriŋkidʒ/ ) of source maps, and errors in the original mapping.

## Slide 91
Part Ⅳ——1. Manipulation and transformation of spatial data
(5) Edge matching (边界匹配)
Edge matching always requires some interactive editing. Accordingly, GIS software differs considerably (相当) in the degree of automation provided.

## Slide 92
Part Ⅳ——1. Manipulation and transformation of spatial data
(6) Interactive graphic editing (交互图形编辑)
These functions involve the addition, deletion, moving, and changing of the geographic position of features.
Editing should be possible at any time. Most graphic editing occurs during the data compilation phase (编制阶段, /,kɔmpə'leiʃən/) of any project.

## Slide 93
Part Ⅳ——1. Manipulation and transformation of spatial data
(6) Interactive graphic editing (交互图形编辑)
Many of the editing that is undertaken involves the cleaning up of topological errors identified earlier. The capability to snap to existing elements, e. g. nodes and arcs, is critical.
The functionality of graphic editing does not differ greatly across GIS software offerings. However, the user interface (界面) and ease of use (易用性) of the editing functions usually does.

## Slide 94
P116-Questions:
1. How many phases may the acquisition of attribute data be divided into?
2. Does the initial acquisition of data require the efforts of many different agencies?
3. What is the common approach to collect attribute data?
4. Which kind of field registration of attribute data has become usual and popular in recent years?
5. What should the data fields(字段) of the registration forms (表格) correspond to?

## Slide 95
Translate the sentences into English:
1. 最常用的删除碎片的方法是允许用户为数据层定义优先级和一个容差值。
2. 大多数GIS软件要求参与数据分析的数据层的地图投影一致，否则就必须进行变换。
3. GPS的精度不仅取决于量测方法，也取决于测站之间的距离、量测时间以及卫星相对于被测点的位置。
4. 以弧线/节点方式获取数据有助于建立拓扑结构，减少了后期处理量。
5. 空间数据和属性数据都存在多种类型的数据源，最常见的空间数据源有：硬拷贝地图、航空摄影照片、遥感影像。

## Slide 96
Translations:
1. The most common method to remove slivers is allowing the user to define a priority for data layers in combination with a tolerance value.
2. Most GIS software requires that data layers for analysis must be in the same map projection. If not, transformation must be required.
3. In addition to measuring methods, accuracy is dependent on the distance between stations, measuring time and the satellite’s position in relation to the point to be determined.
4. Data capture in an arc/node approach helps to build a topologic data structure. This lessens the amount of post process.
5. A wide variety of data sources exist for both spatial and attribute data. The most common sources for spatial data are: hard copy map, aerial photographs, remote sensing images.

## Slide 97
Part Ⅳ——2. Integration and modeling of spatial data
The integration(/,inti'greiʃən/) of data provides the ability to answer complex spatial questions that could not be answered otherwise.
Often, these are inventory (明细，清单/’invəntri/) or locational questions such as how much? Or where? Answers to locational and quantitative questions require the combination of several different data layers to be able to provide a more complete and realistic (现实的, /,riə’listik/) answer. The ability to combine and integrate data is the backbone (基础，支柱) of GIS.

## Slide 98
Part Ⅳ——2. Integration and modeling of spatial data
Often, applications do require a more sophisticated (完备的, /sə’fistikeitid/) approach to answer complex spatial queries and “what if? ” scenarios (/si,neəri:’əu/). The technique used to solve these questions is called spatial modeling (空间模型).

## Slide 99
Part Ⅳ——2. Integration and modeling of spatial data
While some explicit analytical models do exist, especially in natural resource applications, most modeling formulae (formula的复数/ 'fɔ:mjəli:/ ) are determined based on the needs of a particular project. The capability to undertake complex modeling of spatial data, on an ad hoc basis (特定的基础), has helped the resource specialists (专家) to further understanding of the natural environment, and the relationship between selected characteristics of that environment.

## Slide 100
Part Ⅳ——2. Integration and modeling of spatial data
The use of GIS spatial modeling tools in several traditional resource activities has helped to quantify (量化) processes and define models for deriving (派生) analysis products. This is particularly true in the area of resource planning and inventory compilation (编制明细数据/,kɔmpə’leiʃən/ ).

## Slide 101
Part Ⅳ——2. Integration and modeling of spatial data
Most GIS users are able to better organize their applications because of their interaction(交互作用) with the use of GIS technology.
The utilization of spatial modeling techniques requires a comprehensive(充分地) understanding of the data sets involved, and the analysis requirements.

## Slide 102
Part Ⅳ——2. Integration and modeling of spatial data
The raster data model has become the primary spatial data source for analytical modeling with GIS (GIS分析模型). The raster data model is well suited to the quantitative analysis of numerous data layers. To facilitate (/fə’siliteit/) these raster modeling techniques most GIS software employs a separate module (模块，/’mɔdju:l/) specifically (特有地，专门地/spə'sifikli/) for cell processing.

## Slide 103
Part Ⅳ——3. Integrated analytical functions in a GIS
Most GIS provide the capability to build complex models by combining primitive (原始的/’primətiv/) analytical functions. Systems vary as to (根据) the complexity provided for spatial modeling, and the specific functions that are available (可用的).
However, most systems provide a standard set of primitive analytical functions that are accessible (可理解的，易用的) to the user in some logical (符合逻辑的，合乎常理的) manner.

## Slide 104
Part Ⅳ——3. Integrated analytical functions in a GIS
Aronoff (阿罗诺夫) identifies four categories of GIS analysis functions.
(1) Retrieval (检索), reclassification (重分类), and generalization (综合)
(2) Topological overlay techniques
(3) Neighborhood (邻域) operations
(4) Connectivity (连接性) functions.

## Slide 105: 专业词汇
1、地理信息系统
2、航空照片，航空摄影
3、数字遥感
4、数字线划地图
5、数字高程模型
6、统计数据
7、数字图象处理
8．专题图层
9．空间要素
10．高分辨率
11．拓扑重建
12．拓扑建立
13．矢量-栅格转化
14．能见度分析
15．悬挂线
16．不正规多边形
17．交互核对，交叉检查
18．地面控制点
19．坐标稀疏化
20．几何变换
21．地图投影变换
22．多边形叠加
23．容差值
24．拓扑叠加
25．邻域分析
26．属性归纳或综合
27．定量分析
28．实时差分GPS
29．数字化仪分辨率
30. 地图比例尺

## Slide 106: 专业词汇
1、地理信息系统
2、航空照片，航空摄影aerial photography
3、数字遥感
4、数字线划地图
5、数字高程模型
6、统计数据
7、数字图象处理digital image processing
8．专题图层 thematic layers
9．空间要素 spatial features
10．高分辨率 high resolution
11．拓扑重建 re-building of the topology
12．拓扑建立
13．矢量-栅格转化 vector-to-raster conversion
14．能见度分析visibility analysis
15．悬挂线 dangling arcs
16．不正规多边形weird polygons
17．交互核对，交叉检查 cross checking
18．地面控制点 ground control points
19．坐标稀疏化Coordinate thinning
20．几何变换Geometric transformations
21．地图投影变换 Map projection transformations
22．多边形叠加 polygon overlay
23．容差值 tolerance value
24．拓扑叠加Topological overlay
25．邻域分析Neighborhood operations
26．属性归纳或综合attribute generalization
27．定量分析 quantitative analysis
实时差分GPS real-time differential GPS
数字化仪分辨率digitizer resolution

## Slide 107
Part Ⅳ——3. Integrated analytical functions in a GIS
(1) Retrieval, reclassification, and generalization
Perhaps the initial(最初的) GIS analysis that any user undertakes is the retrieval and/or reclassification of data.
Retrieval operations occur on both spatial and attribute data. Often data is selected by an attribute subset (子集) and viewed graphically (通过图表). Retrieval involves the selective search (选择性搜索), manipulation, and output of data.

## Slide 108
Part Ⅳ——3. Integrated analytical functions in a GIS
(1) Retrieval, reclassification, and generalization
Reclassification involves the selection and presentation (报告，呈现) of a selected layer of data based on the classes or values of a specific attribute, e. g. land use. It involves looking at an attribute, or a series of attributes, for a single data layer and classifying the data layer based on the range of values of the attribute.

## Slide 109
Part Ⅳ——3. Integrated analytical functions in a GIS
(1) Retrieval, reclassification, and generalization
Accordingly, features adjacent (邻近的，毗邻的，/ə'dʒeisnt/) to one another that have a common value, e. g. species, but differ in other characteristics, e. g. tree height, will be treated and appear as one class.
In raster based GIS software, numerical value(数值) are often used to indicate classes. Reclassification is an attribute generalization (属性归纳或综合) technique.

## Slide 110
Part Ⅳ——3. Integrated analytical functions in a GIS
(1) Retrieval, reclassification, and generalization
In a vector based GIS, boundaries between polygons of common reclassed values should be dissolved to create a cleaner map of homogeneous (同类的/,hɔmə‘dʒi:niəs/) continuity (连续性 /,kɔnti'nju:əti/).
Raster reclassification intrinsically (从本质上, /in’trinzikli/) involves boundary dissolving. The dissolving of map boundaries based on a specific attribute value often results in a new data layer being created. This is often done for visual clarity(清晰度) in the creation of derived maps.

## Slide 111
Part Ⅳ——3. Integrated analytical functions in a GIS
(1) Retrieval, reclassification, and generalization
Almost all GIS software provides the capability to easily dissolve boundaries based on the results of a reclassification.
Some systems allow the user to create a new data layer for the reclassification while others simply dissolve the boundaries during data output.

## Slide 112
Part Ⅳ——3. Integrated analytical functions in a GIS
(1) Retrieval, reclassification, and generalization
One can see how the querying capability of the DBMS(数据库管理系统) is a necessity in the reclassification process.
The ability and process for displaying the results of reclassification, a map or report, will vary depending on the GIS.
In some systems the querying process is independent from data display functions, while in others they are integrated.

## Slide 113
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
The capability to overlay multiple data layers in a vertical fashion is the most required and common technique in geographic data processing.
In fact, the use of a topological data structure can be traced(追溯) back to the need for overlaying vector data layers.
With the advent(出现,到来 /’ædvent/) of the concepts of mathematical topology polygon overlay has become the most popular geoprocessing(空间数据处理) tool, and the basis of any functional GIS software package.

## Slide 114
Raster datasets in practical use can be very large. As an example, satellite remote sensing data is frequently used to distinguish categories of land cover over large areas. The standard view of the earth from the U.S.’s Landsat series of satellites covers approximately 30,000 square kilometers, which at a pixel size of 30 meters, corresponds to approximately 35 million raster cells or pixels(像素).
When dealing with such large datasets, there are several algorithms used to compress the data. Some of these algorithms are completely reversible (可逆的/ ri'və:səbl/); that is, we may recover exactly the original datasets. Others minimize the volume of the stored data by losing a small and controlled amount of the original information.
Fast reading

## Slide 115
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
Topological overlay is predominantly (/pri’dɔminəntli/) concerned with overlaying polygon data with polygon data, e. g. soils and forest cover.
However, there are requirements for overlaying point, linear, and polygon data in selected combinations, e. g. point in polygon, line in polygon, and polygon on polygon are the most common.

## Slide 116
—常见的矢量叠加分析的类型有：
  相交叠加
  面面叠加：求取两个多边形图层中任意两个多边形交叠的部分——结果是一个多边形图层(intersect)
  线面叠加：用多边形图层中的多边形切割线图层中的每条线——结果是所有落在多边形内的折线图层
  点面叠加：用多边形图层中的多边形切割点图层——结果是所有落在多边形内的点组成的点图层
  点线叠加：和点面类似，所有在线的给定距离缓冲区内的所有点组成结果图层
  2、合并叠加
  面面叠加合并：将两个多边形图层融合、合并为一个图层union

## Slide 117
— 常见的矢量叠加分析的类型有：
  3、擦除叠加
  任意两种（点、线、面）图层之间可进行擦除操作：消除第一个图层中落在第二图层地物及其缓冲区中的部分，而形成新的图层
  4、标识叠加
  点面叠加、线面叠加、面面叠加
  将与第一个图层的地物相交、包含的多边形的属性信息附加到第一个图层的对应地物上
  可用于解决“查找某条河流穿越的省份有哪些？”这样的问题

## Slide 118
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
Vector and raster based software differ considerably(相当，非常) in their approach to topological overlay.
Raster based software is oriented towards (面向/’ɔ:riənt/) arithmetic (算法/ə’riθmətik/) overlay operations, e. g. the addition, subtraction, division (/di'viʒn/), multiplication (/,mʌltipli’keiʃn/) of data layers.

## Slide 119
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
The nature of the one attribute map approach, typical (典型特征) of the raster data model, usually provides a more flexible (灵活的) and efficient overlay capability. The raster data model affords a strong numerically modeling (quantitative analysis, 定量分析) capability.
Most sophisticated (复杂的，深奥的/sə’fistikeitid/) spatial modeling is undertaken within the raster domain(领域).

## Slide 120
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
In vector based systems topological overlay is achieved by the creation of a new topological network from two or more existing networks.
This requires the rebuilding of topological tables, e. g. arc, node, polygon, and therefore can be time consuming and CPU intensive (CPU占用率高).

## Slide 121
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
The result of a topological overlay in the vector domain is a new topological network that will contain attributes of the original input data layers.
In this way selected queries can then be undertaken of the original layer, e. g. soils and forest cover, to determine where specific situations occur, e. g. deciduous (落叶的/di’sidʒuəs/) forest cover where drainage (排水系统/'dreinidʒ/) is poor.

## Slide 122
Part Ⅳ——3. Integrated analytical functions in a GIS
(2) Topological overlay
Most GIS software makes use of a consistent logic for the overlay of multiple data layers. The rules of Boolean logic(布尔逻辑/’bu:liən/) are used to operate on the attributes and spatial properties of geographic features.
Boolean algebra (布尔代数 /’ældʒibrə/) uses the operators (操作符号) AND, OR, XOR (异或), NOT to see whether a particular condition is true or false. Boolean logic represents all possible combinations of spatial interaction (相互作用) between different features. The implementation (工具) of Boolean operators is often transparent (显而易见) to the user.

## Slide 123
Erase

## Slide 124
Part Ⅳ——3. Integrated analytical functions in a GIS
(3) Neighborhood operations
Neighborhood operations evaluate (评价/i’væljueit/) the characteristics of an area surrounding a specific location.
Virtually (实际上/’və:tʃuəli/) all GIS software provides some form of neighborhood analysis. A range of different neighborhood functions exist.
The analysis of topographic features is normally categorized (归类/’kætəgəraiz/) as being a neighborhood operation.

## Slide 125
Part Ⅳ——3. Integrated analytical functions in a GIS
(3) Neighborhood operations
This involves a variety (归类/və’raiəti/) of point interpolation (插值/in,tə:pə’leiʃn/) techniques including slope and aspect calculations, contour generation, and thiessen polygons (泰森多边形) .
Interpolation is defined as the method of predicting unknown values using known values of neighboring locations. Interpolation is utilized most often with points based elevation data.

## Slide 128
Part Ⅳ——3. Integrated analytical functions in a GIS
(3) Neighborhood operations
Elevation data usually takes the form of (以…形式出现) irregular or regular spaced points (间隔的点).
Irregularly space points are stored in a Triangular Irregular Network (TIN, 不规则三角网/trai’æŋgjələ/). A TIN is a vector topological network of triangular facets (小平面 /'fæsit/) generated by joining the irregular points with straight line segments.
The TIN structure is utilized when irregular data is available, predominantly in vector based systems. TIN is a vector data model for 3D data.

## Slide 129
Part Ⅳ——3. Integrated analytical functions in a GIS
(3) Neighborhood operations
Without doubt the most common neighborhood function is buffering.
Buffering involves the ability to create distance buffers around selected features, be it points, lines, or areas.
Buffers are created as polygons because they represent an area around a feature.
Buffering is also referred to as (被认为) corridor (通道，廊道/'kɔridɔ:/) or zone generation with the raster data model.

## Slide 130
Part Ⅳ——3. Integrated analytical functions in a GIS
(3) Neighborhood operations
Usually, the results of a buffering process are utilized in a topological overlay with another data layer.
For example, to determine the volume (/’vɔlju:m/) of timber (木材/'timbə/) within a selected distance of a cutline, the user would first buffer the cutline data layer.

## Slide 131
Part Ⅳ——3. Integrated analytical functions in a GIS
(3) Neighborhood operations
They would then overlay the resultant (产生的/ri'zʌltənt/) buffer data layer, a buffer polygon, with the forest cover data layer in a clipping fashion.
This would result in a new data layer that only contained the forest cover within the buffer zone.
Since all attributes are maintained in the topological overlay and buffering processes, a map or report could then be generated.

## Slide 132
Fast Reading
In any information system, facilities must be provided to detect and correct errors in the database. Different kinds of errors are common in different data sources. To illustrate some of the common varieties, we will discuss some of the errors that must be detected when generating a vector dataset, whether developed from manual digitizing or an automated scanner.
Polygonal areas, by definition, have closed boundaries. If a graphic object has been encoded as a polygon, the boundary must be continuous. Software should be able to detect that a polygon is not closed. Causes for this kind of error included encoding error and digitizing error(either points along the boundary of the polygon, or connections between the points, are missing).
With some systems, the boundaries between adjacent polygons may have to be digitized twice. Such systems create slivers and gaps. Slivers occur when the adjacent polygons apparently overlap; gaps occur when there is apparent space between adjacent polygons.

## Slide 133
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
Most often these include the analysis of surfaces and networks.
Connectivity functions include proximity analysis (邻近度分析/prɔk‘siməti/), network analysis (网络分析), spread (扩散) functions, and three dimensional surface analysis (三维表面分析/di’menʃənəl /) such as visibility (可见度/,vizə’biləti/) and perspective viewing (透视图).

## Slide 134
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
This category of analysis techniques is the least developed (最不发达) in commercial GIS software.
Consequently (因此), there is often a great difference in the functionality offered between GIS software offerings.
Raster based systems tend to focus on linear network analysis capabilities.

## Slide 135
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
However, this appears to be changing as GIS software becomes more sophisticated (/sə’fistikeitid/), and multi-disciplinary (多学科的/,mʌlti'disəplineri/) applications require a more comprehensive and integrated functionality.
Some GIS offerings provide both vector and raster analysis capabilities. Only in these systems will one fund(提供) a full range of connectivity analysis techniques.

## Slide 136
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
Proximity analysis techniques are primarily (首要地/prai'merəli/) concerned with the proximity of one feature to another.
Usually proximity is defined as the ability to identify any feature that is near any other feature based on location, attribute value, or a specific distance.
A simple example is identifying all the forest stands that are within 100 meters of a gravel (砾石/'ɡrævl/) road.

## Slide 137
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
It is important to note that neighborhood buffering is often categorized as being a proximity analysis capability.
Depending on the particular GIS software package, the data model employed, and the operational architecture (运算方式/'ɑ:kitektʃə/) of the software it may be different to distinguish proximity analysis and buffering.

## Slide 138
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
Proximity analysis is often used in urban based applications to consider areas of influence, and ownership queries.
Proximity to roads and engineering(设计) infrastructure (基础设施/’infrəstrʌktʃə/) is typically important for development planning, tax calculations, and utility (公用事业) billing (安排).

## Slide 139
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
The identification of adjacency (邻接，相邻/ə’dʒeisənsi/) is another proximity analysis function.
Adjacency is defined as the ability to identify any feature having certain attributes that exhibit adjacency with other selected features having certain attributes. A typical example is the ability to identify all forest stands of a specific type, e. g. species, adjacent to a gravel (沙砾, 砾石) road.

## Slide 140
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
Network analysis is a widely used analysis technique.
Network analysis techniques can be characterized(描述，以…为特征) by their use of feature networks. Feature networks are almost entirely composed of linear features.
Hydrographic hierarchies(等级制度/’haiərɑ:ki/) (水网) and transportation(运输，转移/,trænspɔ:’teiʃən/) networks(交通网) are prime examples.

## Slide 141
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
Three dimensional analysis involves a range of different capabilities.
The most utilized is the generation of perspective(透视) surfaces. Perspective surfaces are usually represented by a wire frame diagram(图解) reflecting profiles (剖面/'prəufail/) of the landscape. These profiles viewed together, with the removal of hidden lines, provide a three dimensional view.

## Slide 142
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
Most GIS software packages offer 3-D capabilities in a separate module. Several other functions are normally available. These include the following functions:
①user definable vertical exaggeration(夸张手法/ig,zædʒə’reiʃn/), viewing azimuth (方位角/,æziməθ/), and elevation angle;
②identification of viewsheds(视域), e. g. seen versus(相对) unseen areas;
③the draping(遮盖/ei/) of features, e. g. point, lines, and shaded polygons onto the perspective surface;

## Slide 143
Part Ⅳ——3. Integrated analytical functions in a GIS
(4) Connectivity analysis
These include the following functions:
④generation of shaded relief(地貌晕渲) models simulating illumination(模拟光照/i,lu:mi’neiʃn/);
⑤generation of cross section(横截面) profiles;
⑥presentation of symbology (符号/sim'bɔlədʒi/ ) on the 3-D surface;
⑦line of sight perspective views (视线景观) from user defined viewpoints (视角).

## Slide 144
This menu provides access(访问) to the ERDAS IMAGINE Image Interpreter (图像解译器/in’təpritə/) functions. It opens when you click the Interpreter icon (图标/'aikɔn/) in the ERDAS IMAGINE icon panel.
※※Image Interpreter

## Slide 145
Spatial Enhancement (空间增强/in’hɑ:nsmənt/): Click to access functions for enhancing images using the values of individual and surrounding pixels. —convolution(卷积/,kɔnvə’lu:ʃn/), texture (纹理分析/’tekstʃə/), resolution merge (分辨率融合/,rezə’lu:ʃn/), statistical filter (统计滤波/'filtə/)
Radiometric Enhancement (辐射增强/,reidiəu’metrik/): Click to access functions for enhancing images using the values of individual pixels within each band. —LUT stretch(查找表拉伸/stretʃ/), histogram match (直方图匹配/’histəgræm/), noise reduction (降噪处理)
※※Image Interpreter

## Slide 146
Spectral Enhancement (光谱增强/’spektrəl/): Click to access functions for enhancing images by transforming the values of each pixel on a multiband basis. —principal components(主成分变换/kəm’pəunənt/), tasseled cap(缨帽变换/’tæsl/), indices(指数计算/’indisi:z/)
HyperSpectral Tools (高光谱工具/haipəs’pektrəl/): Click to access basic and advanced functions applicable(适当的，可应用的/ə’plikəbl/) to hyperspectral data. —spectral profile(光谱剖面), spectral library(光谱数据库)
※※Image Interpreter

## Slide 147
Fourier Analysis (傅里叶变换分析/’furiei/): Click to access functions for enhancing images using Fourier transformations.
Topographic Analysis (地形分析/,tɔpə’ɡræfik/): Click to access functions applicable to elevation data.—shaded relief(地形阴影), painted relief (彩色地势), topographic normalize(地形校正)，viewshed(视域分析)
※※Image Interpreter

## Slide 148
GIS Analysis (GIS分析): Click to access functions for use on thematic data layers (专题数据图层/θi’mætik/). —neighborhood, clump(聚类分析), sieve(过滤分析/siv/), eliminate(剔除处理), matrix(矩阵/’meitriks/), recode(重编码)
Utilities (实用功能): Click to access some common utilities used on raster layers.
※※Image Interpreter

## Slide 149
Change Detection (变化监测): Select this option to compute the differences between two images and to highlight(突出，强调) changes that exceed a user-specified(指定的) threshold(阈值/'θreʃhəuld/).
Functions (函数分析): Select this option to process an input file using one of many mathematical functions in the Spatial Modeler Language such as SIN, COS, etc.
※※Image Interpreter—Utilities

## Slide 150
Operators (代数运算): Select this option to perform simple image algebra(代数/’ældʒibrə/ ) functions on two input images.
Layer Stack (图层组合): Select this option to create a new output file by stacking layers from two or more different input images.
Subset (子区操作,裁切): Select this option to create a new file by subsetting an input file.
※※Image Interpreter—Utilities

## Slide 151
Rescale (数值调整): Select this option to rescale data in any bit format.
Mask (掩膜): this option to use an .img file to select (mask) specific areas from a corresponding .img file.
Degrade (图像退化，降低分辨率): Select this option to reduce the resolution of an image.
※※Image Interpreter—Utilities

## Slide 152
Replace Bad Lines (去除坏线): Select this option to replace bad scan lines in raster data.
Vector To Raster (矢栅转换): Select this option to convert a vector coverage to a raster coverage.
Reproject (投影变换): Select this option to resample(重采样) an image into a different projection.
※※Image Interpreter—Utilities

## Slide 153: ※※Classification
Classification is the process of sorting(分类) pixels into a finite(有限的/’fainait/) number of individual classes, or categories of data, based on their data file values.
If a pixel satisfies a certain set of criteria (标准，规则/krai'tiəriə/), then the pixel is assigned to the class that corresponds to that criteria.

## Slide 154: ※※Classification
For the first part of the classification process, the computer system must be trained to recognize patterns(样本) in the data.
Training is the process of defining the criteria by which these patterns are recognized. The result of training is a set of signatures (模板/’signətʃə/), which are criteria for a set of proposed classes.

## Slide 155: ※※Classification—Signature Editor
There are two ways to classify pixels into different categories:
Supervised(/'su:pəvaiz/)
unsupervised
Many of the Classification tools can also be accessed through the Signature Editor.

## Slide 156: ※※Classification—Signature Editor
The ERDAS IMAGINE Signature Editor allows you to create, manage, evaluate, edit, and classify signatures (.sig extension). The following types of signatures can be defined:
parametric (statistical/,pærə’metrik/参量) —数学模型
nonparametric (feature space特征空间) —无数学模型

## Slide 157: ※※Classification—Signature Editor
parametric (statistical /,pærə'metrik/)
For parametric signatures the following decision rules are provided:
• maximum likelihood (最大似然)
• Mahalanobis distance (马氏距离)
• minimum distance (最小距离)

## Slide 158: ※※Classification—Signature Editor
nonparametric (feature space特征空间)
If the signature is non-parametric (i.e., feature space AOI), then the following decision rules are offered:
• feature space (特征空间)
• parallelepiped (平行六面体/,pærəle'lepiped/)
With non-parametric signatures, you must also decide the overlap rule and the unclassified rule.

## Slide 159: ※※Classification—Signature Editor
In order to create signatures, you must have the image you are classifying opened in a Viewer.
Then, using the AOI tools, you can create point, line, polygon, and "seed" areas of interest.
To enter an AOI into the Signature Editor, first select it, then select Edit > Add from the Signature Editor menu bar or click the icon(图标/’aikɔn/) on the Signature Editor tool bar.

## Slide 160: ※※Classification—Signature Editor
When all of the signatures are entered, you can use the Edit, View, and Evaluate(/i'væljueit/) menu options(选项) to evaluate and edit your signatures.
When you are satisfied with the signatures, use the Classify menu to actually perform the image classification.

## Slide 161: ※※Classification—Unsupervised
ERDAS IMAGINE uses the ISODATA(迭代自组织数据分析技术) algorithm to perform an unsupervised classification.
ISODATA stands for “Iterative Self-Organizing Data Analysis Technique.” It is iterative(迭代/’itərətiv/) in that it repeatedly performs an entire classification and recalculates statistics.

## Slide 162: ※※Classification—Unsupervised
The ISODATA clustering method uses the minimum spectral distance formula(最小光谱距离公式) to form clusters.
It begins with either arbitrary(随机的，任意的) cluster means or means of an existing signature set, and each time the clustering repeats, the means of these clusters are shifted. The new cluster means are used for the next iteration(迭代，重复/,itə’reiʃn/).

## Slide 163: ※※Classification—Unsupervised
The ISODATA utility repeats the clustering of the image until either:
a maximum number of iterations has been performed, or
a maximum percentage of unchanged pixels has been reached between two iterations.

## Slide 164
ISODATA Arbitrary Clusters
ISODATA First Pass
ISODATA Second Pass

## Slide 165: 专业词汇
1、网络分析
2、邻近度分析
3、三维表面分析
4、直方图匹配
5、光谱增强
6、空间信息
7、土地信息系统
8．拓扑结构
9．关联属性数据
10．能见度分析
11．派生数据
12．人工数字化
13．硬拷贝地图
14．线跟踪
15．目测
16．比例尺修正
17．拉伸变形
18．交互核对
19．全站经纬仪
20．边界匹配
21．交互图形编辑
22．地图综合
23．线要素化简
24．数据优先级
25．图幅
26．空间建模
27． GIS分析模型
28．数据重分类
29．边界融合
30．插值分析
31．不规则三角网
32．图像解译

## Slide 166: ※※Classification—Evaluating
After a classification is performed, these methods are available for testing the accuracy of the classification:
Thresholding(定义阈值/’θreʃhəuld/)—Use a probability image file to screen(筛选) out misclassified (错分的)— pixels.
Accuracy Assessment—Compare the classification to ground truth or other data.

## Slide 167: ※※Classification—Evaluating
Thresholding
Thresholding is the process of identifying the pixels in a classified image that are the most likely to be classified incorrectly.
These pixels are put into another class (usually class 0). These pixels are identified statistically, based upon the distance measures that were used in the classification decision rule.

## Slide 168: ※※Classification—Evaluating
Thresholding
In a minimum distance classification, each distance value is the Euclidean(欧氏) spectral distance between the measurement vector of the pixel and the mean vector of the pixel’s class.
In a Mahalanobis distance or maximum likelihood classification, the distance value is the Mahalanobis distance between the measurement vector of the pixel and the mean vector of the pixel’s class.

## Slide 169
卡方/'kaiskweə/

## Slide 170
It shows how the histogram(/’histəgræm/) of the distance image usually appears. This distribution is called a chi-square distribution, as opposed to a normal distribution (正态分布), which is a symmetrical(对称的/si’metrikl/) bell curve.
Histogram of a Distance Image
The pixels that are the most likely to be misclassified have the higher distance values at the tail of this histogram. At some point that you define—either mathematically or visually—the tail of this histogram is cut off. The cutoff point is the threshold.

## Slide 171: ※※Classification—Evaluating
Thresholding
To determine the threshold:
• interactively change the threshold with the mouse, when a distance histogram is displayed while using the threshold function. This option enables you to select a chi-square value by selecting the cut-off value in the distance histogram, or
• input a chi-square parameter or distance measurement, so that the threshold can be calculated statistically.

## Slide 172
Interactive Thresholding Tips(提示)

## Slide 173: ※※Classification—Evaluating
Accuracy Assessment
Accuracy assessment is a general term for comparing the classification to geographical data that are assumed to be true, in order to determine the accuracy of the classification process. Usually, the assumed-true data are derived from ground truth data.

## Slide 174: ※※Classification—Evaluating
Accuracy Assessment
It is usually not practical to ground truth or otherwise test every pixel of a classified image. Therefore, a set of reference pixels is usually used. Reference pixels(参考像元) are points on the classified image for which actual data are (or will be) known. The reference pixels are randomly selected.

## Slide 175: ※※Classification—Evaluating
Accuracy Assessment——Random Reference Pixels
When reference pixels are selected by the analyst, it is often tempting to select the same pixels for testing the classification that were used in the training samples.
This biases(偏离/’baiəs/) the test, since the training samples are the basis of the classification. By allowing the reference pixels to be selected at random, the possibility of bias is lessened or eliminated.

## Slide 176: ※※Classification—Evaluating
Accuracy Assessment——Random Reference Pixels
The number of reference pixels is an important factor in determining the accuracy of the classification. It has been shown that more than 250 reference pixels are needed to estimate the mean accuracy of a class to within plus or minus five percent.

## Slide 177: ※※Classification—Evaluating
Accuracy Assessment——CellArray
An Accuracy Assessment CellArray (矩阵) is created to compare the classified image with reference data.
This CellArray is simply a list of class values for the pixels in the classified image file and the class values for the corresponding reference pixels. The class values for the reference pixels are input by you.

## Slide 178: ※※Classification—Evaluating
Accuracy Assessment——Error Reports
From the Accuracy Assessment CellArray(矩阵), two kinds of reports can be derived.
• The error matrix simply compares the reference points to the classified points in a c × c matrix, where c is the number of classes (including class 0).
• The accuracy report calculates statistics of the percentages of accuracy, based upon the results of the error matrix.

## Slide 179: ※※Classification—Evaluating
Accuracy Assessment——Kappa Coefficient (/,kəuə’fiʃənt/)
The Kappa coefficient expresses the proportionate(成比例的/prə'pɔ:ʃənət/) reduction in error generated by a classification process compared with the error of a completely random classification.
For example, a value of .82 implies that the classification process is avoiding 82 percent of the errors that a completely random classification generates.

## Slide 180
两幅栅格图的kappa计算公式为 k = (Po-Pc)/(1-Pc)
设栅格总像元数为n，真实栅格为1的像元数为a1，为0的像元数为a0，模拟栅格为1的像元数为b1，为0的像元数为b0，两个栅格对应像元值相等的像元数为s，则
Po = s/n， Pc = (a1*b1+a0*b0)/(n*n)

## Slide 181: ※※Data preparation
Create New Image (生成单值图像)—create a single or multilayer image that contains a single data value.
Create Surface (创建三维地形表面)—create a surface layer or DEM from input point elevations, merge(融合/mə:dʒ/) and split DTMs(Digital terrain model).

## Slide 182: ※※Data preparation
Subset Image (图像分幅裁剪)—create and define a subset image.
Subset Definition (/,defi’niʃən/) : Use this group to define a rectangular(矩形的/rek’tæŋɡjulə/) area of the data to be used as the output file. The coordinates of the subset may be derived from an inquire box (查询框/in'kwaiə/) in the Viewer or by entering explicit X,Y values for the upper-left and lower-right corners of the subset. The default coordinates are the entire input file.

## Slide 183: ※※Data preparation
Subset Image (图像分幅裁剪)—create and define a subset image. ——four corners
UL X: Upper-left X coordinate
UL Y: Upper-left Y coordinate
LR X: Lower-right X coordinate
LR Y: Lower-right Y coordinate
UR X: Upper-right X coordinate
UR Y: Upper-right Y coordinate
LL X: Lower-left X coordinate
LL Y: Lower-left Y coordinate

## Slide 184: ※※Data preparation
The use of the Four Corners option produces a subset in a way similar to the use of an AOI. In the illustration below, the marks in red show the locations of the four corners. The white box shows the largest rectangle that includes all four points. This is the area that will be subset using the Four Corners option.

## Slide 185: ※※Data preparation
Dice Image (图像方块裁剪)—take a large image and chip out new images at your specified dimensions(尺寸, 面积, 维/di’menʃən/). This enables you to specify the collar(衣领，关键) extent so that neighboring new images are overlapped with each other.

## Slide 186: ※※Data preparation
Image Geometric Correction (图像几何校正/,dʒi:ə’metrɪk /)—select the image you want to rectify(校正/'rektifai/).

## Slide 187: ※※Data preparation
Mosaic Images (图像拼接处理/məu’zeiik /)—mosaic two or more images together. The images must be rectified and/or calibrated(校准，标准化/'kælibreitid/).

## Slide 188: ※※Data preparation
Reproject Images (图像投影变换)—resample(重采样/ri:'sæmpl/) an image into a different projection.
Gauss-Kruger map projection高斯－克吕格地图投影
transverse Mercator projection横轴墨卡托投影

## Slide 189: ※※GIS’s development
GIS’s development has been more evolutionary(进化的), than revolutionary(创新的). It responds to contemporary needs as much as it responds to technical breakthroughs. Planning and management have always required information as the cornerstone.
Early information systems relied on physical storage of data and manual processing. With the advent of the computer, most of these data and procedures have been automated. As a result, the focus of GIS has expanded from descriptive inventories to entirely new applications involving prescriptive(规范性) analysis.

## Slide 190: ※※GIS’s development
In this transition, map analysis has become more quantitative. This wealth of new processing capabilities provides an opportunity to address(处理，解决) complex spatial issues in entirely new ways.
It is clear that GIS technology has greatly changed our perspective of a map. It has moved mapping from a historical role of provider of input, to an active and vital ingredient(要素) in the “thruput” (解决能力) process of decision-making.
Today’s professional is challenged to understand this new environment and formulate innovative(创新的) applications that meet the complexity and accelerating needs of the twenty-first century.

## Slide 191: ※※What Can You Do with GIS?
1. Map Where Things Are Lets you find places that have the features you're looking for.
2. Map Quantities People map quantities to find places that meet their criteria and take action. A children’s clothing company might want to find ZIP Codes (邮递区号) with many young families with relatively high income. Public health officials might want to map the numbers of physicians per 1,000 people in each census tract (调查区域) to identify which areas are adequately served, and which are not.

## Slide 192: ※※What Can You Do with GIS?
3. Map Densities A density map lets you measure the number of features using a uniform areal unit so you can clearly see the distribution. This is especially useful when mapping areas, such as census tracts or counties, which vary greatly in size. On maps showing the number of people per census tract, the larger tracts might have more people than smaller ones. But some smaller tracts might have more people per square mile—a higher density.

## Slide 193: ※※What Can You Do with GIS?
4. Find What’s Inside Use GIS to monitor what’s happening and to take specific action by mapping what’s inside a specific area. For example, a district attorney(律师/ə’tə:ni/) would monitor drug-related arrests to find out if an arrest is within 1,000 feet of a school—if so, stiffer penalties (更严厉的惩罚/'penəlti/) apply.
5. Find What's Nearby GIS can help you find out what's occurring within a set distance of a feature by mapping what's nearby.

## Slide 194: ※※What Can You Do with GIS?
6. Map Change Map the change in an area to anticipate(预测) future conditions, decide on a course of action, or to evaluate the results of an action or policy. By mapping where and how things move over a period of time, you can gain insight into how they behave. For example, a meteorologist(气象学家/,mi:tiə’rɔlədʒist/) might study the paths of hurricanes(飓风/'hʌrikən/) to predict where and when they might occur in the future.

## Slide 195
Google Earth
Google 公司
World Wind
NASA
Yahoo Maps
Yahoo 公司
MSN Virtual Earth
微软
ArcGIS Explorer
ESRI
SkylineGlobe
Skyline 公司
GeoGlobe
武汉大学
DEPS CAS、GeoBeans3D
中科院遥感所
Digital Earth Platforms：

## Slide 196
A map projection is a system in which locations on the curved surface of the earth are displayed on a flat sheet or surface according to some set of rules.
Angles, areas, directions, shapes and distances become distorted when transformed from a curved surface to a plane(平面). All these properties cannot be kept undistorted in a single projection. Usually the distortion in one property will be kept to a minimum while other properties become very distorted.
The most common methods of projection can be conceptually described by imagining the developable surface, which is a surface that can be made flat by cutting it along certain lines and unfolding or unrolling(展开，铺开) it.
The actual shape of the earth can now be determined quite accurately by observing satellite orbits. Satellite systems, such as GPS, can determine latitude and longitude at any point on the earth's surface to accuracies of fractions of a second.
Fast reading

## Slide 197: Beidou upgrades for global reach
China has begun to upgrade its Beidou Navigation Satellite System with global-coverage capabilities through the launch of new satellites.
Beidou is the world's fourth navigation satellite system, following GPS in the United States, GLONASS in Russia and Galileo in the European Union.
The new-generation satellites feature better accuracy, stability and signal clarity than previous Beidou models thanks to improvements in intersatellite links, laser communication devices and atomic clocks(原子钟). They will also be more compatible with GPS, GLONASS and Galileo.
By the end of 2018, China will have launched 18 third-generation Beidou satellites into space to cover all nations involved in the Belt and Road Initiative (一带一路). The Beidou system now covers nearly 30 countries.
According to plans from the China Satellite Navigation Office, the network will be made up of more than 30 satellites before the end of 2020 - several now in orbit will be decommissioned（使退役） by then - to give Beidou global coverage.

## Slide 198: Extraction and analysis of coastline of Fujian province based on RS and GIS
Coastline is an important identity of border between land and water. Coastal zone is the first marine economic regions of China. It is important to study the coastline changes due to the significance of coastal ecosystem. In this paper, Landsat TM / ETM remote sensing image data of Fujian in 2002,2006 and 2010 was used. Based on RS( remote sensing) and GIS technology,the coastline was respectively extracted with methods of visual interpretation and automatic interpretation. The coastline changes and its reasons were analyzed and summarized based on overlay analysis and statistics. It showed that the total coastline in Fujian province during 2002 and 2010 had increased 291. 84 km and it kept on growing. Great changes of coastline are in areas of Sansha Bay and in vicinity of Quanzhou in addition to the changes in Xiamen Island. Landfill, sedimentation, port and fishery infrastructure constructions are important factors for the coastline growth.

## Slide 199
基于遥感和GIS的福建省海岸线的提取和变化研究
海岸线是陆地和水体交界的重要标识,海岸带是我国第一海洋经济区域,研究海岸线的变化对海岸带生态环境研究具有重要的意义.本研究利用遥感和GIS技术获取了福建省2002、2006、2010年3个时期的Landsat TM/ETM遥感影像数据,采用目视解译和自动解译的方法分别提取出了各时期的福建省海岸线,进行叠加分析,对比统计3个时期福建省海岸线的变化特征和变化程度,总结分析了其变化趋势和变化原因.结果表明,在2002~2010的8a时间里,福建省的海岸线长度整体为增长趋势,共计增长了291.84 km,三沙湾区域和泉州附近变化较大,厦门岛内变化也较大.其中泥沙淤积、填海造地、港口建设和渔业设施建设这4个因素为主要增长因素.